## Slide 1
Electrical Circuit Analysis
This lesson will introduce you to electrical circuits that combine series circuits and parallel circuits.
You will also learn how to analysis this circuits to solve for unknown quantities

## Slide 2
Learning Goals
By the end of this lesson, you will be able to:
draw circuit analysis cards
apply Kirchhoff’s laws to combination circuits
analysis combination circuits
solve problems involving combination circuits

## Slide 3
Success Criteria
Can I:
draw circuit analysis cards
apply Kirchhoff’s laws to combination circuits
analysis combination circuits
solve problems involving combination circuits

## Slide 4
Circuit Analysis Cards
whenever you analyse a circuit, you must convey the
information and results in a circuit analysis card.

## Slide 5
Circuit Analysis Steps
STEP 1a: Fill in any known quantities in your circuit analysis card
STEP 1b: Fill in any “buried” known quantities. These quantities are the ones you can assume at a glance from
KL
STEP 2: Reduce any parallel element to a series equiv.
STEP 3: Draw the circuit as a series equivalent circuit and calculate the total resistance by adding up the resistors.

## Slide 6
STEP 4: Use V = IR to find any missing variable if you are given any two out of three variables in a row of the card
STEP 5: According to KCL, all series resistors have the same current. Fill in these currents in the card.
STEP 6: Repeat STEP 4.
STEP 7: Use KVL to determine any unknown voltages.
STEP 8: Repeat STEP 4.

## Slide 7
Sample Problem
Analyse the following circuit
Vo = 120. V
R1 = 5.00 W
R4 = 20.0 W
R2 = 10.0 W
R3 = 15.0 W

## Slide 8
Sol’n:
Step 1a:
Step 1b: can’t be done

## Slide 9
Step 2: R2 and R3 are in parallel

## Slide 10
Step 3:
Vo = 120. V
R1 = 5.00 W
R4 = 20.0 W
R2-3 = 6.0 W
RT = R1 + R2-3 + R4 = 31.0 W

## Slide 11
Step 4: Use Ohm’s Law to find Io

## Slide 12
Step 5:
According to KCL: I1 = I2-3 = I4 = IT = 3.87 A

## Slide 13
Step 6: Use Ohm’s Law to find V1 , V4

## Slide 14
Step 7: Use KVL to find V2 , V3

## Slide 15
Step 8: Use Ohm’s Law to find I2 , I3

## Slide 16
HOMEWORK
Read Section 11.6, 11.8
Review Tutorials in the sections
Questions 1 pg 532
      1 pg 534
      1 – 4 pg 535